## Slide 1
HPC AI Observability
and Security
Architecture Reference | Open Source Sovereign Stack
Samuel Desseaux | Erythix / Aureonis
1
HPC Cluster Architecture
Physical topology: nodes, NVLink, InfiniBand, storage, scheduler
2
Training Step Timeline
Data load, forward, backward, AllReduce — what really happens
3
Observability Stack
Collection, storage, visualization — open source sovereign pipeline
4
Security Threat Surface
6 attack vectors specific to HPC AI and their detection methods

## Slide 2
CHAPTER 01 | FOUNDATION
What is HPC, and why does AI need it?
Samuel Desseaux | Erythix / Aureonis | HPC AI Observability and Security
HPC (High Performance Computing) assembles hundreds to thousands of machines for problems too large for a single computer. Since 2018, training large language models has become the dominant HPC workload. These models require staggering amounts of compute and memory that no single machine can provide.
GPT-3
3,500
GPU-days to train
Llama 3 70B
140 GB
minimum memory to load
H100 SXM5
3.35 TB/s
GPU HBM bandwidth
A laptop has 16 GB RAM and 8 GB GPU memory. Llama 70B needs ~140 GB just to fit its weights — and thousands of GPU-hours to train. A single machine is structurally incapable of meeting this need.
CPU | Generalist
8 to 128 powerful cores at 3-6 GHz. Excellent branch prediction and arbitrary memory access. Essential for orchestration, I/O, and control flow.
Poorly suited for massive matrix operations.
GPU | Specialist
10,000 to 18,000 CUDA cores at 1-2 GHz. High Bandwidth Memory (HBM) at 3.35 TB/s. All cores execute the same simple operation simultaneously.
Purpose-built for the matrix multiplications at the core of AI.

## Slide 3
CHAPTER 02 | ARCHITECTURE
How an HPC cluster is built — 5 Fundamental Layers
Samuel Desseaux | Erythix / Aureonis | HPC AI Observability and Security
L1
GPU Compute Nodes
4 to 8 GPUs per node, interconnected by NVLink (600 GB/s). Each GPU has 80 GB HBM3. 2 CPUs for orchestration, 512 GB RAM, local NVMe for staging.
dcgm-exporter
thermal attack
HBM bound
L2
HPC Interconnect: InfiniBand / RoCE
InfiniBand HDR at 400 Gb/s, sub-microsecond latency. Fat-Tree topology guarantees non-blocking bandwidth. Gradients flow here during NCCL AllReduce.
ibstat / perfquery
RDMA blind spot
latency critical
L3
Parallel Shared Storage: Lustre / GPFS
Files striped across dozens of OSS servers. 28+ GB/s aggregate throughput. GPUs must never wait for data — compute/IO ratio is the key sizing metric.
Lustre metrics
data poisoning
throughput
L4
Job Scheduler: SLURM / PBS
Manages queues, GPU allocation, job isolation, environment setup. Prolog/epilog scripts allow instrumentation injection at job boundaries.
slurm-exporter
job isolation
scheduling
L5
ML Software Stack: CUDA / PyTorch / NCCL
CUDA/ROCm driver, PyTorch or JAX, NCCL for collective communications. Runs in Docker or Singularity containers — isolation, reproducibility, GPU privilege risks.
PyTorch profiler
supply chain
NCCL tuning

## Slide 4
CHAPTER 03 | HOW IT WORKS
What really happens during distributed training
Samuel Desseaux | Erythix / Aureonis | HPC AI Observability and Security
1
Data Load + H2D
Workers read from Lustre, tokenize and normalize data, load into pinned CPU memory. DMA transfer to GPU via PCIe (~8-16 GB/s). Must overlap with previous batch computation. If slow: I/O bound workload.
2
Forward Pass
Data traverses model layer by layer. Each layer is primarily matrix multiplication. GPU decomposes work into tiles across Streaming Multiprocessors. Activations stored in HBM for backward pass reuse.
3
Backward Pass
Model computes loss against ground truth, propagates error backward via chain rule. Each GPU computes local gradients on its own data subset. Gradients differ across GPUs.
4
AllReduce (NCCL)
Ring-AllReduce averages gradients across all GPUs over InfiniBand. After N rounds, every GPU holds the full sum. 15-40% of step time. The straggler makes everyone wait at the sync barrier.
5
Optimizer Step
AdamW updates all parameters in parallel using averaged gradients with adaptive correction. 7B parameters updated simultaneously on the GPU. Cycle repeats for next batch.
Key insight: GPU utilization reported at 87%. Effective compute: ~19% of step time. NCCL AllReduce alone: 43%. The straggler effect can reduce global efficiency by 30% without triggering any alert.

## Slide 5
CHAPTER 04 | OBSERVABILITY
Observability: seeing what really happens at every layer
Samuel Desseaux | Erythix / Aureonis | HPC AI Observability and Security
M
Metrics
Numerical time-series: GPU SM utilization, HBM bandwidth, step time, NCCL latency, IB retransmits. Stored in VictoriaMetrics. Enable alerting and trend analysis.
L
Logs
Timestamped events with context: CUDA errors, NCCL warnings, SLURM interruptions, OOM kills. Aggregated in Loki. Provide qualitative context that metrics cannot capture.
T
Traces
End-to-end tracking across all nodes and processes. Identify exactly on which node and in which function time is lost. Essential for diagnosing stragglers.
COLLECT
(per node)
dcgm-exporter | node-exporter | OTel Collector | Falco / Tetragon | slurm-exporter | ibstat scripts
STORE
(centralized)
VictoriaMetrics (metrics, 90d) | Loki (logs, 30d) | Tempo / Jaeger (traces, 7d) | AlertManager
VISUALIZE
(Grafana)
GPU Cluster Dashboard | Network + Storage | ML Training Metrics | Security Events | SLURM Jobs

## Slide 6
CHAPTER 04 | eBPF
eBPF: observing without instrumenting
Samuel Desseaux | Erythix / Aureonis | HPC AI Observability and Security
eBPF allows attaching verified programs to thousands of kernel instrumentation points: system calls, GPU driver ioctls, network events, file access — with negligible overhead. Observe training processes from the outside, without modifying any code.
Trace CUDA allocations from a Python process
bpftrace -e 'kprobe:cuMemAlloc /pid == $1/ { printf("alloc %d bytes\n", arg1); }'
Detect unexpected outbound network connections from ML processes
bpftrace -e 'tracepoint:syscalls:sys_enter_connect
/comm == "python3"/ { printf("connection: %s\n", ntop(args->uservaddr)); }'
Watch checkpoint directory reads
bpftrace -e 'tracepoint:syscalls:sys_enter_openat
/str(args->filename) startswith "/checkpoints"/
{ printf("[%s] reads %s\n", comm, str(args->filename)); }'
Falco and Tetragon build on eBPF for production-grade security: Falco detects and alerts on suspicious kernel behavior in real time. Tetragon enforces syscall policies per process — blocking unauthorized CUDA ioctls, network calls, or checkpoint reads before they complete.

## Slide 7
CHAPTER 05 | SECURITY
Security of AI workloads on HPC: 6 threat vectors
Samuel Desseaux | Erythix / Aureonis | HPC AI Observability and Security
Critical assets: model weights (IP), training data (sensitive), compute infrastructure (multi-tenant). HPC differs from classic datacenters: GPU requires privileged kernel access, opening unique attack surfaces.
PyPI Supply Chain
Malicious CUDA kernel in Python package. Exfiltrates weights during backward pass.
DETECT: Private registry + hash all deps
Data Poisoning
Modify Lustre files between integrity check and DataLoader read. Backdoor insertion.
DETECT: SHA-256 per shard at read time
RDMA Blind Spot
Peer memory read via RDMA. No firewall, IDS, or iptables sees this traffic.
DETECT: IB anomaly metrics + behavioral baseline
Gradient Injection
Federated training: send crafted gradients to introduce backdoor in final model.
DETECT: Gradient norm distribution + KL divergence
VRAM Leakage
GPU memory not zeroed between SLURM jobs. Previous tenant weights readable.
DETECT: Pre-job GPU wipe + driver configuration
Container Escape
CVE-2024-0132 in nvidia-container-toolkit. Escape to host, access all workloads.
DETECT: Falco rules + Tetragon syscall policy

## Slide 8
CHAPTER 06 | REFERENCE
Open source tooling: the sovereign stack
Samuel Desseaux | Erythix / Aureonis | HPC AI Observability and Security
VictoriaMetrics
METRICS
High-perf time-series DB, Prometheus-compatible. Handles hundreds of millions of active series with 5-10x lower memory than native Prometheus.
dcgm-exporter
GPU METRICS
Exposes GPU metrics via DCGM API: SM utilization, HBM bandwidth, ECC errors, NVLink throughput, power. Mandatory entry point.
OpenTelemetry
TRACES + LOGS
CNCF standard for instrumentation. Python SDK for PyTorch, OTLP protocol, Collector routing to any backend.
Grafana
VISUALIZATION
Universal dashboard. Natively connects to VictoriaMetrics, Loki, Tempo. Correlated views of metrics, logs, and traces.
Loki
LOGS
Log aggregation indexing labels only. LogQL queries. Very efficient for SLURM, NCCL, and Python framework logs.
Falco
RUNTIME SECURITY
eBPF-based behavioral anomaly detection. Detects suspicious file access, unexpected connections, binary modifications in real time.
Tetragon
RUNTIME SECURITY
Cilium eBPF security. Enforces per-process syscall policies. Blocks unauthorized operations before they complete.
SLURM
SCHEDULING
Dominant HPC scheduler for 20 years. Manages queues, GPU allocation, job isolation. Prolog/epilog for instrumentation injection.

## Slide 9
CHAPTER 06 | REFERENCE ARCHITECTURE
Complete reference architecture: zero vendor dependency
Samuel Desseaux | Erythix / Aureonis | HPC AI Observability and Security
COLLECT
(per node)
dcgm-exporter + node-exporter + OTel Collector + Falco / Tetragon + slurm-exporter
STORE
(central)
VictoriaMetrics + Loki + Tempo + AlertManager
VISUALIZE
Grafana dashboards + AlertManager routing + Grafana OnCall
Zero vendor lock-in. All tools are open source, self-hosted, and auditable. Data never leaves your infrastructure. Full digital sovereignty.